## Slide 1
DOCTORAL DISSERTATION DEFENSE
Enhanced Decision Support System for
Wildfire Disaster Response and Management
DISASTERAWARE
PRESENTED BY
Çağlar Akman
SUPERVISOR
Prof. Dr. Mehmet Kemal Leblebicioğlu
DEPARTMENT OF
Electrical and Electronic Engineering
Graduate School of Natural and Applied Sciences
Middle East Technical University · Ankara

## Slide 2
OUTLINE
Presentation Roadmap
01
Ch. 1
Motivation & Research Gaps
Wildfire DSS landscape · G1–G8 architectural gaps
02
Ch. 1
Research Question & Hypotheses
Central RQ · main hypothesis · H1 · H2 · H3
03
Ch. 2–3
Problem Formulation & Background
Formal DSS problem · fuzzy reasoning · distributed DSS
04
Ch. 4
DisasterAware Simulation Framework
Grid domain · hybrid fire model · external data layers
05
Ch. 5
System Specification
6 features · fuzzy design · 4 concepts · 9× rule reduction
06
Ch. 6
Implementation Architecture
Layered DSS · coordination · explainability & governance
07
Ch. 7
Experiments & Results
3 scenarios · centralized baseline · H1/H2/H3 evaluation
08
Ch. 8
Conclusion & Future Work
C1–C8 ↔ G1–G8 closure · directions forward
DisasterAware · PhD Defense

## Slide 3
AT A GLANCE · 01
Motivation, Gaps, Research Question & Hypotheses
MOTIVATION
Wildfires are among the most consequential 21st-century hazards — yet existing DSS architectures remain structurally mismatched with dynamic, partially observable, resource-constrained wildfire response.
EIGHT ARCHITECTURAL GAPS IN EXISTING WILDFIRE DSS
G1
Closed
decision space
G2
Centralized
architecture
G3
Epistemic
uncertainty
G4
Limited
explainability
G5
Sim–decision
coupling
G6
Operational
constraints
G7
Spatio-temporal
integration
G8
Hierarchical
coordination
RESEARCH QUESTION
How can a distributed, explainable DSS generate adaptive and operationally feasible intervention guidance under partial observability in dynamic wildfire environments?
MAIN HYPOTHESIS · three testable sub-claims
H1 ADAPTABILITY
Distributed agents yield faster spatial response and better resource allocation than centralized DSS.
targets G1 · G2 · G7 · G8
H2 INTERPRETABILITY
Concept-driven fuzzy reasoning enables traceable, inspectable decisions at cell level.
targets G3 · G4 · G5
H3 FEASIBILITY
Cost-aware fuzzy evaluation keeps interventions operationally executable under dynamic constraints.
targets G3 · G6

## Slide 4
CONTRIBUTIONS · 02
Eight Architectural Contributions of DisasterAware
Each contribution targets a specific gap identified in Chapter 1.
C1 Open decision space
Concept-driven fuzzy reasoning generates intervention guidance dynamically — no predefined alternatives.
closes G1
C2 Distributed architecture
Layered DSS with region-local fuzzy reasoners + global coordination layer.
closes G2
C3 Epistemic uncertainty
Fuzzy inference encodes partial observability via graded membership — no prior distributions required.
closes G3
C4 Explainable reasoning
Rule-level traceability + AI governance layer (audit log, operator override).
closes G4
C5 Sim / decision separation
Simulation Core and DSS Core are architecturally independent; DSS never writes to system state.
closes G5
C6 Operational constraints
Cost-aware fuzzy evaluation integrates resource availability, travel time, and access.
closes G6
C7 Spatio-temporal reasoning
Propagation field Ψₖ and ignition time τₖ feed spatially-directional, time-sensitive features.
closes G7
C8 Hierarchical coordination
Local → coordination → governance levels mirror operational, tactical, and strategic decision layers.
closes G8

## Slide 5
GAP ↔ CONTRIBUTION MAPPING · 03
One-to-One Structural Closure of the Eight Gaps
ONE-TO-ONE ARCHITECTURAL MAPPING
G1 Closed decision space
→
C1 Open decision space
G2 Centralized architecture
→
C2 Distributed architecture
G3 Epistemic uncertainty
→
C3 Fuzzy uncertainty encoding
G4 Limited explainability
→
C4 Explainable reasoning
G5 Sim–decision coupling
→
C5 Sim / DSS separation
G6 Operational constraints
→
C6 Cost-aware evaluation
G7 Spatio-temporal integration
→
C7 Spatio-temporal fuzzy
G8 Hierarchical coordination
→
C8 Multi-level architecture
HYPOTHESES ↔ CONTRIBUTIONS
H1 Adaptability
addressed by C1 · C2 · C7 · C8 · covering G1 · G2 · G7 · G8
H2 Interpretability
addressed by C3 · C4 · C5 · covering G3 · G4 · G5
H3 Feasibility
addressed by C3 · C6 · covering G3 · G6
Every gap G1–G8 is closed by ≥1 contribution and evaluated by ≥1 hypothesis.

## Slide 6
PROBLEM FORMULATION · 04
Wildfire DSS as a Distributed, Partially Observable Decision Process
SYSTEM EVOLUTION (physical dynamics)
DECISION GENERATION
FEASIBILITY & QUALITY
CLOSED-LOOP STRUCTURE (Figure 2.1)
State → Observation → Distributed local DSS → Global coordination → Feasibility / quality check → Feedback into external inputs.
Remark 2.1 The problem is computationally intractable under exact optimization — single-step action space ≥ 57500 · state is continuous · εk lacks known distribution. Hence satisficing QDSS,k ≥ ηk, not global optimization.

## Slide 7
SIMULATION FRAMEWORK · 05a
Layered Architecture — Physics, Decision, Interaction Separated
Figure 4.1 · Simulation Framework block diagram
1
External Data Sources
input layer
Meteorology · topography · fuel · ignition · DSS output. Boundary conditions — never written by DSS core.
2
Simulation Core
physics
Authoritative physics engine. Grid State Manager + Hybrid Fire Spread Model update Sₖ → Sₖ₊₁.
3
Decision Support Core
cognition
Observes 𝒪ₖ from Sₖ; produces intervention U_DSS,k. Separate from physics (Contribution C5).
4
Web UI Dashboard
supervision
Asynchronous operator interface. Scenario control via ΘUI — inputs only, no state overwrite.

## Slide 8
SIMULATION FRAMEWORK · 05b
Hybrid Fire Spread Model — Deterministic + Stochastic Dynamics
Per-cell state sₖ(x,y) evolves through four coupled updates. Physical realism comes from three mechanisms: persistence · propagation from neighbours · external ignition.
BURNING STATUS persistence · propagation · ignition
Cell ignites if cumulative neighbour influence Ψₖ exceeds Θ_ign, or if externally triggered.
FUEL MASS combustion + suppression
Simultaneous depletion: combustion B·F_burn and DSS-driven suppression F_red (through f_supp).
FIRE INTENSITY bounded combustion proxy
Bounded strength indicator; modulates suppression resistance and DSS features — does NOT drive propagation directly.
IGNITION TIME temporal memory τₖ
Records time since combustion began; feeds feature z₆ (urgency) and explainability, not fire physics.
Transition is deterministic; stochasticity enters only through exogenous inputs (e.g., wind gusts). All DSS-driven influence is mediated by F_red (suppression) — the DSS never writes state variables directly.

## Slide 9
SIMULATION FRAMEWORK · 05c
External Data Layers & Spatio-Temporal State Representation
INPUT STRUCTURE (Eq. 31 · Eq. for F_DSS)
FIVE FORCING LAYERS + TWO DECISION CONTEXTS
U_Meteo,k
Meteorology
wind speed, direction, gust · humidity · temperature · precipitation
U_Geo
Topography
elevation · slope · aspect · accessibility
U_Fuel,k
Fuel
vegetation class · combustible mass · moisture
U_Ign,k
Ignition
binary spatio-temporal injection field
U_DSS,k
DSS actions
suppression capacity · availability · effectiveness · travel time
U_Val,k
Asset values
priority score V_prio · critical facility index V_crit
U_Res,k
Resources
contextual resource state used for decision evaluation
CELL STATE sₖ(x,y)
Bₖ burning status
∈ {0,1}
F_load,k available fuel mass
∈ [0,1]
Iₖ intensity proxy
∈ [0,1]
τₖ time since ignition
discrete-time memory
grid-based Ω ⊂ ℝ²

## Slide 10
THEORETICAL BACKGROUND · 06
Why Fuzzy Reasoning for Wildfire DSS?
FUZZY INFERENCE SYSTEM (FIS)
Crisp thresholds are brittle near boundaries — fuzzy membership is smooth and robust to observation noise.
COMPARATIVE ASSESSMENT (Table 5.2)
Criterion
Bayes
D–S
NN
Fuzzy
No prior distribution required
○
●
●
●
Handles epistemic uncertainty
○
●
○
●
Rule-level traceability
○
○
○
●
Linguistic interpretability
○
○
○
●
Real-time feasibility
○
●
◐
●
No training data required
●
●
○
●
Operator override at rule level
○
○
○
●
● supports ◐ partial ○ not supported
TAKEAWAY Fuzzy logic is the only paradigm satisfying all seven DisasterAware requirements — directly closing G3, G4 and enabling rule-level operator override.

## Slide 11
SYSTEM SPECIFICATION · 07a
From Operational Questions to a 6-Feature Input Space
FOUR OPERATIONAL QUESTIONS
Q1 How severe is the fire threat?
Combustion intensity + spread potential
uses I_k, Ψ_k
Q2 Can we effectively intervene?
Travel time, access, availability, fuel resistance
uses R_time, R_avail, G_access, F_load
Q3 What is the asset exposure?
Priority-weighted proximity to active fire front
uses V_prio, Ψ_k, B_k
Q4 How urgent is the action?
Temporal fire progression + composite threat
uses τ_k, c1·c2·c3
SIX DERIVED FEATURES z₁…z₆ ∈ [0,1]
z₁
Fire intensity
I_k
Q1
z₂
Fuel load
F_load,k
Q1·Q2
z₃
Spread potential
min(1, Ψ_k / Ψ_ref)
Q1·Q3
z₄
Asset exposure
V_prio · B_k^δ
Q3
z₅
Resource accessibility
R_avail · exp(-β_t·R_time) · G_access
Q2
z₆
Temporal urgency
1 − exp(−λ·τ_k/τ_ref)
Q4
All features bounded in [0,1] via physically meaningful normalizations — a uniform fuzzy variable design applies to every feature (Section 5.2.1).

## Slide 12
SYSTEM SPECIFICATION · 07b
Fuzzification & Four Situational Concepts
MEMBERSHIP FUNCTION TEMPLATE (uniform design, Nμ = 3)
Partition of unity: every feature value is resolved into Low/Medium/High with membership summing to 1 — ensures deterministic aggregation at the concept layer.
CONCEPT CONSTRUCTION (Section 5.2.3)
Figure 5.x · Features → situational concepts (first-order c₁·c₂·c₃; second-order c₄)
c₄ is a second-order concept — it re-fuzzifies c₁,c₂,c₃ together with temporal urgency z₆, closing the threat → feasibility → exposure → urgency reasoning chain.

## Slide 13
SYSTEM SPECIFICATION · 07c
Rule Base Complexity — A Proven 9× Reduction
Naive direct-FIS design would require Nμ^Nfeat rules per intervention. Concept abstraction reduces the inference space from 6 features to 4 concepts (Proposition 5.3).
DIRECT FIS (BASELINE)
729
rules per intervention · 3⁶
total rule base: 2,187
CONCEPT-MEDIATED (DISASTERAWARE)
81
rules per intervention · 3⁴
total rule base: 351
9×
reduction
FORMAL DERIVATION
TAKEAWAY Concept abstraction makes the rule base manageable, validatable, and distributed — without sacrificing expressiveness. Each of 81 rules is hand-inspectable by domain experts.